## Slide 1: Mass transport modelling with GRACE and GRACE-FO
Frank Flechtner
Helmholtz Centre Potsdam, GFZ German Research Centre for Geosciences, Potsdam
Section 1.2 „Global Geomonitoring and Gravity Field“
Webinar, 13.08.2019

## Slide 2: Mass Transport Monitoring from Space
GRACE = Gravity Recovery and Climate Experiment
The twin satellites and their relative motion in space are the experiment!
GRACE and it´s successor GRACE Follow-on (GRACE-FO) are the only missions to monitor mass transport in system Earth
Mass transport is related to climate change related issues such as variations in the global water cycle (ground water depletion, droughts, flooding), ice melting in large glacier systems or sea level rise.

## Slide 3: Measurement Principle (1)
Courtesy: D. Schütze (AEI Hannover)
Gravitational Law: where 1=Earth, 2=Satellite

## Slide 4: Measurement Principle (2)
Courtesy: D. Schütze (AEI Hannover)

## Slide 5: Measurement Principle (3)
Courtesy: D. Schütze (AEI Hannover)

## Slide 6: Measurement Principle and KBR Accuracy
Accuracy: 1μm = 12 digits
Distance: ca. 220,000000000 km

## Slide 7: GRACE Instruments and Observations
Observation of gravitationally caused orbit perturbations along the common line of sight of a twin satellite pair by
high-low (GPS) and
low-low (K-Band) Satellite-to-Satellite Tracking (SST)
Observation of non-gravitational accelerations by 3D Accelerometer
Observation of the satellite and instrument orientation by Star Cameras
Validation of GPS-derived orbit by Satellite Laser Ranging (SLR)

## Slide 8: Coarse Principle of Gravity Field Determination (1)
Unknown parameters, incl. spherical harmonic coefficients, are obtained e.g. by dynamical orbit determination and least squares adjustment.
Observations are the geometric difference of the (observed) real orbit from a (theoretical, computed) reference orbit = o-c
1 day
15 days
30 days

## Slide 9: Coarse Principle of Gravity Field Determination (2)
To derive the global gravity field of the Earth the satellite orbit is numerically integrated in an
inertial reference system
For this we need
  Approximate initial position and velocity of the satellite
  Disturbing (gravitational, non-gravitational, empirical) forces acting on the satellites
By variation of the initial values of position and velocity we get an orbit which is best adjusted to the satellite orbit observations (o-c).
From the remaining observation residuals o-c of the adjustment process we get the gravitational potential U represented by (time dependent) spherical harmonic coefficients Clm(t)/Slm(t)
zonal
Zonal
l=6
m=0
Sectorial
l=9
m=9
Tesseral
l=16
m=9

## Slide 10: Time Variations of the Gravity Field
September 2006
100
0
-100
100
0
-100
August 2006
Change: Aug to Sep 2006 (Factor ~1:10.000)
1mGal =10-5 m/s2

## Slide 11: GRACE: 15 Years of Amazing Discoveries
2018

## Slide 12: GRACE: 15 Years of Amazing Discoveries

## Slide 13: GRACE and Hydrology
Monitoring of Continental Hydrological Cycle
Close the global Water Balance
ΔTWS(t) = Total Water Storage
ΔGW(t) = Ground Water
ΔSW(t) = Surface Water
ΔSWE(t) = Snow Water Equivalent
ΔSM(t) = Soil Moisture
ΔRO(t) = Run Off
} ΔAW(t) = Accessible Water
can only be provided by GRACE!
From archives, e.g.
SM from NASA Global Land Data Assimilation System
SWE from NOAA Snow Data Assimilation System
or satellites, e.g.
SMOS, SMAP
}
Courtesy: IGG Bonn
ΔTWS(t) = ΔGW(t) + ΔSW(t) + ΔSWE(t) + ΔSM(t) - ΔRO(t)
[cm EWH]

## Slide 14: Greenland vs. Antarctica
Source: CCI Greenland, CCI Antarctica Gravimetry Mass Balance Products, data1.geo.tu-dresden.de
Mass [Gt]
4
8
4
8
Entire Greenland
Mass [Gt]
Entire Antarctica
22
6
22
6
Mean rate of change
(08/2002–07/2016)
[mm w.e./yr]

## Slide 15: GRACE and Altimetry for Sea Level Rise Monitoring

## Slide 16: GRACE-FO
NASA and GFZ responded to science community call for a continuation mission (GRACE Follow-On).
Initial discussions in 2009/2010
Funding in Germany secured 2012
GRACE-FO launched on May 22, 2018.

## Slide 17: GRACE-FO in a Nutshell
Nominal GRACE-FO Launch:
May 22, 2018
Launch-Early Orbit Phase (LEOP):
May-22 – May-26, 2018
In-Orbit-Checkout (IOC):
May-27, 2018 – Jan-27, 2019
First Science Data:
May 30, 2018
Start of Science Phase ( E ):
Jan 28, 2019
First Level-1 Data Delivery:
May 28, 2019
First Level-2 Data Delivery:
Jul 26, 2019

## Slide 18: GRACE-FO Laser Ranging Interferometer (Tech Demo)

## Slide 19: GRACE-FO LRI Data (Example GFZ Processing)
26 June 0-24h
26 June 0-1.5h

## Slide 20: What can be expected from the GRACE-FO LRI?
Flechtner et al. (2016): What Can be Expected from the GRACE-FO Laser Ranging Interferometer, Surv. in Geoph.